## Slide 1: Planning for the Unexpected: Manure Storage and Natural Disasters
Kevin Erb
University of Wisconsin – Madison
Division of Extension
kevin.erb@wisc.edu

## Slide 2: Storage Issues - Solid
Spontaneous combustion (fire) – and the runoff from fire control.
Barn fires – and the runoff from fire control.
Floodwaters – ponding around stored manure in fields or dry lots

## Slide 3: Storage Issues - Liquid
Overtopping storage (excess rain/flooding event) or poor management.
Barn fires – adding unexpected water to storage.
Structural failure – Cracks, rodents, construction errors / non-engineered modifications.

## Slide 4: Iowa Summary
304 manure spills from within 10 yr (1992-2002)
Armstrong et al. 2010
Graphic: Armstrong et al 2001. Photos: UWEX, IA DNR, EPA

## Slide 5: Wisconsin Summary
Ronk and Erb, 2010
Chart: 
| Farm | Transportation | Land Application
 | 153 | 95 | 102
Notes: Farm includes all aspects of the manure handling system – reception pits, lots, manure storage, piping, pumps, etc. Land application includes incidents that occurred at the time of application and those that occurred later (as a result of rain, snowmelt, or ponding)

## Slide 6: Wisconsin On-Farm Incidents
Top months for overflow: August, April
Ronk and Erb, 2010
Chart: 
| Storage overflow | Storage leak/mechanical | Lot runoff, other
 | 58 | 61 | 34
Notes: 65%+ of the incidents involve how manure storage is handled and managed. Due to rounding, percentages may not add up to 100%

## Slide 7: When do Storages Overflow?
Ronk and Erb, 2010, Stencil and Erb, 2015
Chart: 
| Operator Error | Other
 | 46 | 49

## Slide 8: Being Prepared
Determine what are the potential problems you could encounter
Create both a prevention strategy and a response plan for each one
Make sure everyone knows the plan

## Slide 9: Example: Spontaneous Combustion-poultry manure
Determine what are the potential problems you could encounter
Create both a prevention strategy and a response plan for each one
Make sure everyone knows the plan
Photo: https://www.rootsimple.com/2014/10/compost-piles-on-fire/

## Slide 10: Prevention Strategy
Manage pile sizes/airflow/moisture to reduce chances of spontaneous combustion
Site windrow (or barn if under-barn storage) away from water resources
Create a berm to contain/slow down runoff from fire fighting (BEFORE THE FIRE)

## Slide 11: Response Plan
Think through the potential for a fire
  Where will the runoff water go?
  What are options to contain it?
  Where do I put it?

## Slide 12: Example - Storage Leak: 300,000 gallons in 6 hours
Photo: https://www.rootsimple.com/2014/10/compost-piles-on-fire/
Photo: Kevin Erb, UW Extension

## Slide 13: Situation
Construction around pit damaged a stormwater pipe running in storage berm
Pipe collapsed, releasing 300,000+ gallons of manure into road ditch/fields

## Slide 14
Notes: Berm showing drop in south and rise in north pits.

## Slide 15
Notes: Old 57 towards pit view.

## Slide 16
Notes: Cleanup 3.

## Slide 17
Notes: East River trib Mill Road 2.

## Slide 18: Prevention Strategy
Identify risks at time of construction—reroute stormwater pipes and drainage tile
The dangers of gravel backfill around pipes

## Slide 19: Prevention Strategy
Work with a professional engineer when modifying storage
Secondary containment?

## Slide 20: Response Plan
Think through the potential for leak caused by an unknown pipe or a rodent burrow
Where would it flow to? Where is the equipment to contain it? Can I access it quickly?
Where do I put the manure?

## Slide 21
Photo: Kevin Erb, UW Extension
Notes: Pipe plus roadditch at pit 2.

## Slide 22
Photo: Kevin Erb, UW Extension
Notes: Tent city turf 1.

## Slide 23
Photo: Kevin Erb, UW Extension
Notes: Manure slushie 3.

## Slide 24
Photo: Kevin Erb, UW Extension
Notes: Old 57 clean water trib damn 1.

## Slide 25
Photo: Kevin Erb, UW Extension
Notes: Neighbors yard post fire department flush.

## Slide 26
Photo: Kevin Erb, UW Extension
Notes: Old 57 clean water trib damn 1.

## Slide 27
Photo: Kevin Erb, UW Extension
Notes: Solids on snow 1.

## Slide 28: Flooding – Solid
The longer water is in contact with manure, the more nutrient enriched the water becomes
Solid manure piles will leach for weeks after saturation

## Slide 29: Flooding
Do not place manure stacks/storage in areas likely to flood
Keep storage several feet below design capacity to handle unexpected rains/delayed spreading
  For those in Tropical Storm areas, this may be 3-5 feet!
  Wisconsin – several 8+ inch rainfall events

## Slide 30: Always have extra capacity – pump before you need to
Photos: ThinkProgress.org

## Slide 31: Overtopping Storage
Do not “add a few feet of soil”
Find other designed/engineered storage in the neighborhood to use.
  Farms in the upper midwest are known to truck manure 80 miles ONE WAY in crisis situations.

## Slide 32: Overtopping Storage
Municipal sewage treatment plants an option of last resort
Charge by the gallon and by the concentration of contaminants
  Don’t agitate - take the most diluted manure from the top, at the far corner of the storage from the inlet pipe

## Slide 33: Fires
Divert, if possible, clean water from manure storage to avoid overfilling
Alert first responders and regulators to the fact that fire fighting actions may cause a secondary manure problem

## Slide 34: What is your PREVENTION STRATEGY?

## Slide 35
Photo Credit: Wisconsin DNR

## Slide 36
Photo: Kevin Erb, UW Extension

## Slide 39: What is your RESPONSE PLAN ?

## Slide 40: Summary
Consider all potential disaster causes
  Rain-delayed spreading/flooding of storage
  Fire response that causes runoff
  Spontaneous combustion
  Storage failure – engineering failure, pipe failure, rodent burrowing into earthen berm

## Slide 41: Summary
Create both a prevention strategy and a response plan for each one
Make sure everyone knows the plan

## Slide 42: Questions?
Kevin Erb
University of Wisconsin – Madison
Division of Extension
kevin.erb@wisc.edu